## Slide 1: A practical review of math and coding Class #7: Coordinates & mapping

## Slide 2: References
Ryan Abernathey’s Earth and Environmental Earth Science, https://earth-env-data-science.github.io/intro
MATLAB: m_map by Pawlowicz, R., 2020. "M_Map: A mapping package for MATLAB", version 1.4m, [Computer software], available online at http://www.eoas.ubc.ca/~rich/map.html
Python: Cartopy tutorial by Phil Elson who is the creator of Cartopy, https://github.com/SciTools/cartopy-tutorial

## Slide 3: Geospatial map projections and reference systems
Understand basic terminology
Determine what map projections are appropriate for your application
Some tutorials

## Slide 4: Projecting sphere onto a flat surface
Earth is 3D
Sphere
Media is 2D
Paper
Computer monitor
Azimuthal Equal-Area

## Slide 5: Projecting sphere onto a flat surface
Map projection means transformation of coordinates from (longitude, latitude) on the sphere to a location on a plane
Hard to avoid distortion when sphere is transformed into a flat surface
Mercator

## Slide 6: Common metrics of distortion
Area
Distance
Shape
Direction
Scale
Mercator

## Slide 7: Common metrics of distortion
Area
Distance
Shape
Direction
Scale
Azimuthal Equal-Area

## Slide 8: Projection by surface classification
Basic 3 types of projections

## Slide 9: Cylindrical projection
Mercator
Meridians and Parallels are straight and perpendicular

## Slide 10: Cylindrical projection
Mercator
Meridians and Parallels are straight and perpendicular
Figure credit: arcgis.com
Mercator
Transverse cylindrical
Oblique cylindrical

## Slide 11: Azimuthal projection
Parallels are complete circles
Great circles from central point are straight lines
Azimuthal Equal-Area

## Slide 12: Azimuthal projection
Parallels are complete circles
Great circles from central point are straight lines
Azimuthal Equal-Area
Polar
Equatorial
Oblique
Figure credit: arcgis.com

## Slide 13: Azimuthal projection
Parallels are complete circles
Great circles from central point are straight lines
Azimuthal Equal-Area
Gnomonic
Stereographic
Orthographic
Figure credit: arcgis.com

## Slide 14: Conic projection
Albers Equal-Area Conic
Meridians are straight equally-spaced lines
Parallels are circular arcs.

## Slide 15: Projections by conserved metrics
Within each of the 3 types, we can have different projections according to conserved metrics
Conformal (orthomorphic) maps preserve angles locally. Examples: Mercator and Stereographic. Google maps.
Equidistant maps preserve distance from a standard point or line. Examples: Azimuthal equidistant and Plate Carree
Equal-area maps preserves areas but the shape may be distorted. Examples: Albers Equal-Area Conic and Azimuthal Equal-Area

## Slide 16: Projections: other non-preserving
Some projections try to strike some balance to minimize the distortion by not preserving any metrics. Usually, the polar regions get most distortions
Robinson: this is my go-to projection for global coverage
Robinson

## Slide 17: Projection choices
Mapping choice depends on data coverage and extent (regional, global, polar, coastal, basin, etc)
Select projection approach (Azimuthal, Cylindrical or Conic)
Preserving metrics (Conformal, Equidistant, Equal-area)

## Slide 18: Coding procedure
Set up projection coordinate system
Display the data (plot, pcolor, contour, etc)
Display topographic features
Display grid lines etc

## Slide 19: Some data example
Meteorological reanalysis (NCEP reanalysis)
  Daily 2m air temperature for 2020
  netCDF file = self-explaining data format. It contains the metadata together as a part of the dataset
2-minute resolution global topography ETOPO2v2